## Slide 1
Arduino - Spotify
Controller
A Project By:
  Daniel Aviv and Ayal Moran

## Slide 2
Overview
The purpose of this project is to create a more interactive and accessible user experience for Spotify, allowing users to control their music playback through simple hand movements.
Introduction
The system utilizes:
  an Arduino UNO R3 microcontroller.
  Four Ultrasonic sensors (PING))) are used for gesture interpretation.
  Hardware components are simulated on TinkerCAD.
  Python is used to scrape data from the TinkerCAD serial monitor.

## Slide 3
The system design of our project can be divided into three components:
  Hardware design
  Software implementation
  The interface between hardware and software.
System Design
Hardware Design
  Core component: Arduino UNO R3 microcontroller.
  Input: Four Ultrasonic Sensors (PING))) for detecting hand distance.
  Simulation: Hardware setup simulated on TinkerCAD for easy modifications and troubleshooting.
Software Implementation
  Developed in C/C++, designed to run on Arduino UNO R3.
  Continuously monitors ultrasonic sensors for gesture detection.
  Interprets sensor data to determine gestures.
  Performs corresponding actions: play, pause, next track, previous track, volume up, and volume down.
Hardware-Software Interface
  Interface between Arduino and Spotify API through Python script.
  Python script scrapes serial monitor of TinkerCAD for commands sent by Arduino.
  Script sends corresponding request to Spotify API, controlling Spotify playback.

## Slide 4
Gestures

## Slide 5
Gestures
  PLAY
  STOP
  NEXT
  PREVIOUS
  VOLUME UP
  VOLUME DOWN

## Slide 6
Gestures
Play\Stop
Play - [3 , 1]
Stop - [1 , 3]

## Slide 7
Gestures
Next\Previous
Next- [4 , 2]
Previous - [2 , 4]

## Slide 8
Gestures
Vol Up\Vol Down
Vol Up- [1 , 2 , 3 , 4]
Vol Down - [1 , 4 , 3 , 2]

## Slide 9
Gestures
The gestures used to control Spotify:
  Play\Stop
  Next\Previous
  Volume Up\Volume Down

## Slide 10
Gestures
The gestures used to control Spotify:
  Play\Stop
  Next\Previous
  Volume Up\Volume Down

## Slide 11
Implementation
  Setup

## Slide 12
Implementation
  Setup
  Helper Functions:
readSensor()

## Slide 13
Implementation
  Setup
  Helper Functions:
readSensor()
getAction()
Notes: להוריד את הדיבוג בהדפסות

## Slide 14
Implementation
  Setup
  Helper Functions:
readSensor()
getAction()
CheckAction()

## Slide 15
Implementation
  Setup
  Helper Functions:
readSensor()
getAction()
CheckAction()
reset()

## Slide 16
Implementation
  Setup
  Helper Functions:
readSensor()
getAction()
CheckAction()
reset()
  Main Loop

## Slide 17
Last Sensor Trigger
idx = 0;
0
idx % 4 = 0;
0
0
0
SensorsGestures[]
[0]
[1]
[2]
[3]

## Slide 18
Last Sensor Trigger
idx = 1;
3
idx % 4 = 1;
0
0
0
SensorsGestures[]
[0]
[1]
[2]
[3]

## Slide 19
Last Sensor Trigger
getAction() returns: -> 'PLAY'; [3,1]
checkAction() sends 'PLAY' to Serial Monitor and reset();
idx = 2;
3
idx % 4 = 2;
1
0
0
SensorsGestures[]
[0]
[1]
[2]
[3]

## Slide 20
Last Sensor Trigger
idx = 0;
0
idx % 4 = 0;
0
0
0
SensorsGestures[]
[0]
[1]
[2]
[3]

## Slide 21
Last Sensor Trigger
idx = 1;
idx % 4 = 1;
0
0
0
4
SensorsGestures[]
[0]
[1]
[2]
[3]

## Slide 22
Last Sensor Trigger
idx = 2;
idx % 4 = 2;
0
0
4
3
SensorsGestures[]
[0]
[1]
[2]
[3]

## Slide 23
Last Sensor Trigger
idx = 3;
idx % 4 = 3;
0
4
3
4
SensorsGestures[]
[0]
[1]
[2]
[3]

## Slide 24
Last Sensor Trigger
idx = 4;
idx % 4 = 0;
4
3
4
1
SensorsGestures[]
[0]
[1]
[2]
[3]

## Slide 25
Last Sensor Trigger
idx = 5;
idx % 4 = 1;
3
3
4
1
getAction() returns: -> 'STOP'; [1,3]
checkAction() sends 'STOP' to Serial Monitor and reset();
SensorsGestures[]
[0]
[1]
[2]
[3]

## Slide 26
Last Sensor Trigger
idx = 0;
0
idx % 4 = 0;
0
0
0
SensorsGestures[]
[0]
[1]
[2]
[3]

## Slide 27
DEMO

## Slide 28
Conclusion
To sum up, this project shows how we can use hand gestures to interact with apps like Spotify. We've created a simple and fun system that lets you control Spotify with your hand movements. This project is a great example of how combining technology and design can lead to really cool results.

## Slide 29
Special thanks to:
Vladi Budnitski
Dr. Yakov Damatov
Creators
Ayal Moran - moranayal@gmail.com
Daniel Aviv - dani6laviv@gmail.com
Thank You!